## Slide 1
INTRODUCTION
LITCHFIELD, CT
TOWN MEETING #5
September 29, 2026
Michael P. Fortuna, AIA
Principal
Paula Tunney, AIA
Associate
Alicia Rosalie, AIA
Architect
Luis Molina
Emerging Professional

## Slide 2
INTRODUCTION
Town Facilities Review Committee
The mission of the Town Facilities Review Committee shall be to review and evaluate future town facility needs and to recommend the most efficient use of the current Town Hall and Bantam School (Town Hall Annex).
Members:
Barbara Putnam, Chairman
Chris Casiello, Vice-Chairman
Sam Olmstead
Carol Powers
Burke Gibney
Diane Field
Jeff Zullo, BOS Member
Mike Eucalito
Denise Raap, First Selectperson

## Slide 3
PROCESS BACKGROUND
2012: Town Hall Building Committee develops plan for new Town Hall behind existing Town Hall at 74 West Street.
2013: New Litchfield Town Hall proposal rejected at referendum.
2017: The former Litchfield County Courthouse closed, and the Greater Litchfield Preservation Trust develops plans to use it as Town Hall, with an addition on the back of the structure. 80 Doyle Road would be given to Litchfield Housing Trust for affordable housing.
2018: Proposal rejected at referendum.
2020: Town Facilities Review Committee formed to assess underutilized Town-owned property.
2021 (Spring): A survey was distributed to 4,517 residential mailing addresses in Litchfield, with 958 responses received.
2021: Bantam citizens’ group worked with an Architect to conceptualize future uses of the Town Hall Annex.
2024: TLBA retained to study best use of Town Buildings:
  Conditions assessment of Town Hall and Bantam Annex
  Programming analysis of all town departments
  Options and recommendations for rehabilitation and reuse of Bantam Annex

## Slide 4
CONTEXT
Boroughs
Litchfield
Bantam
Villages
E. Litchfield
Northfield
Milton

## Slide 5
OPPORTUNITIES
Implement sustainable strategies, such as eliminating use of fossil fuels, energy reduction, or producing on-site renewable energy.
Restore and preserve some of Litchfield’s architectural history.
Inclusive and Equitable Communities
Thriving Local Economies
Well Stewarded Land and Natural Resources
Vibrant and Creative Cultural Ecosystems
Dynamic and Resilient Planning
Clean and Diverse Transportation Systems and Choices
Renewable and Efficient Energy
Inclusive Engagement, Communication and Education
Strategic Materials Management
Optimal Health and Wellness Opportunities
Healthy, Efficient, and Diverse Housing
Effective, Compassionate Homelessness Prevention
Innovative Strategies and Practices
SustainableCT.org

## Slide 6
History
1954: Constructed as the Bantam Elementary School, designed by Marcel Breuer.
1991: Renovated for the Superior Court.
2017: Litchfield Judicial District Courthouse (new construction) opens in Torrington.
2023: Post Office lease extended, generating $63,000/year in revenue.
BUILDING HISTORY - BANTAM ANNEX

## Slide 7
BUILDING HISTORY - BANTAM ANNEX – PROGRESSIVE ARCHITECTURE

## Slide 8
BUILDING HISTORY - BANTAM ANNEX – PROGRESSIVE ARCHITECTURE
The Bantam Elementary School was featured in the magazine, Progressive Architecture, in January 1954 and February 1957.
The school received an award citation in 1954 in the “Design for Education” category of the magazine.
Basis of Design was Daylight, Efficiency and Cost Control

## Slide 9
BUILDING HISTORY - BANTAM ANNEX

## Slide 10
CONDITIONS ASSESSMENT – BANTAM ANNEX

## Slide 11
CONDITIONS ASSESSMENT - BANTAM ANNEX
Site:
Parking is disproportionate to the current use, and site paving & curbs are generally in poor condition.

## Slide 12
CONDITIONS ASSESSMENT - BANTAM ANNEX
Structure:
Laminated wood beams over loadbearing concrete masonry units (CMU).
The structural steel used for the main entry canopy is sound, but the paint finish is in poor condition.
Portions of the exterior CMU, primarily at outside corners, are damaged or cracking.

## Slide 13
CONDITIONS ASSESSMENT - BANTAM ANNEX
Building Exterior:
Walls:
  Painted CMU.
Windows:
  Wood-framed window systems have rotted in several locations, most commonly along the sills.
  The single-pane glazing is inefficient.
  Exterior wood doors & frames have rotted in some locations, and the paint finishes are generally in poor condition.

## Slide 14
BANTAM ANNEX - ROOF
Building Exterior:
Roof:
  The single-ply EPDM roof is beyond its useful life.
  Flashings are also generally in poor condition.

## Slide 15
CONDITIONS ASSESSMENT - BANTAM ANNEX
Utilities:
The end of the original water tank is visible from inside the Water Service Room.
The building was later connected to City water, so the water tank is no longer in use.
Sewer connection replaced existing septic.
An oil tank is located to the East of the building.

## Slide 16
CONDITIONS ASSESSMENT - BANTAM ANNEX
Utilities:
A transformer and generator are located on separate pads South of the Gym wing.

## Slide 17
CONDITIONS ASSESSMENT - BANTAM ANNEX
M/E/P:
Oil boiler, pumps, and air-handling units (AHU’s) with pneumatic controls.
Mechanical systems are generally beyond their useful life and are inefficient.

## Slide 18
BANTAM ANNEX - COURTYARD
M/E/P:
The large AHU’s located in the courtyard which were used for A/C & dehumidification are no longer in use.
A condensing unit has been installed in the courtyard to serve the mini-split system in the Post Office.

## Slide 19
PROGRAMMING and PLANNING

## Slide 20
TOWN DEPARTMENTS & OFFICES
Departments__________________________
Animal Control
Assessor
Building Department
Education
Emergency Management
Finance Department
Fire Marshal
First Selectman
Land Use
Parks and Recreation
Police Department
Probate Court
Public Works
Registrar of Voters
Sewer Department
Social Services
Tax Collector
Town Clerk
Tree Warden
Recycling Center
Boards and Commissions & Stakeholders_________
Post Office
Sustainable Litchfield
Smart Task Force
Design Review Committee
Housing Authority
Housing Plan Steering Committee
Town Facilities Study Committee
Traffic Safety Community Action Group
Option 5: Recommendation Legend
Located at town Bantam Annex
Located at Town Hall

## Slide 21
PROGRAMMING WORKSHEETS

## Slide 22
TOWN HALL – EXISTING PLANS
UPPER LEVEL
LOWER LEVEL

## Slide 23
BANTAM SCHOOL – EXISTING PLANS

## Slide 24
BANTAM SCHOOL – DEMOLISH AND RELOCATE DEPARTMENTS

## Slide 25
OPTION 1: TOWN HALL AT BANTAM and MULTIPURPOSE SPACE IN LITCHFIELD CENTER

## Slide 26
OPTION 2: MAINTAIN TOWN HALL FUNCTIONS AT CURRENT LOCATIONS WITH DAYCARE AT BANTAM

## Slide 27
OPTION 3: TOWN HALL WITH ADDITION WITH COMMUNITY PROGRAMMING AND ARTS CENTER AT BANTAM

## Slide 28
OPTION 4: MAINTAIN TOWN HALL FUNCTIONS AT CURRENT LOCATIONS WITH APARTMENTS AT BANTAM

## Slide 29
OPTION 5: MAINTAIN TOWN HALL FUNCTIONS AT CURRENT LOCATIONS WITH 4 APARTMENTS AT BANTAM

## Slide 30
OPTION 2A: MAINTAIN TOWN HALL FUNCTIONS AT CURRENT LOCATIONS and DEMOLISH 1960s ADDITION AT BANTAM

## Slide 31
BUILDING UPGRADES – BUILDING ENVELOPE
Masonry Wall R-Values
Existing single wythe masonry wall: R2
New Masonry wall with insulated cavity: R29.5
Glazing R-Values
Existing single pane glazing: R<1.0
New ¾” insulated glazing: R3.5

## Slide 32
BUILDING UPGRADES – HVAC (ELECTRIFICATION) CASE STUDY
DEEP West District HQ

## Slide 33
HISTORIC RESTORATION – TRELLIS AT BANTAM ANNEX

## Slide 34
HISTORIC RESTORATION – BANTAM ANNEX COURTYARD

## Slide 35
HISTORIC RESTORATION – CORRIDOR

## Slide 36
HISTORIC RESTORATION – CLASSROOM

## Slide 37
HISTORIC RESTORATION – MULTIPURPOSE ROOM

## Slide 38
COSTS and PHASING

## Slide 39
ESTIMATE OF PROBABLE COSTS – OPTION 5: RECOMMENDATION
Town Hall: $5.8 M (No Work)
Bantam Full Renovation: $32.8 M

## Slide 40
DIAGRAMMATIC PHASING PLAN AND COST ESTIMATE – OPTION 5
Phasing approach breaks Project into more manageable Projects to be funded over time. Each phase carries its proportion of the following:
Hazardous Materials abatement
Envelope and Finishes Upgrades
Building Electrification and PV
HVAC and Mechanical Systems with Potential for Geothermal Systems

## Slide 41
DIAGRAMMATIC PHASING PLAN AND COST ESTIMATE – OPTION 5
Phase 1: Roof $2.4M
Phase 2: West Wing, Food Pantry: $7.2M

## Slide 42
ESTIMATE OF PROBABLE COSTS – OPTION 5 PHASED APPROACH, CONTINUED
Phase 3: East Wing- Apartments $13.5 M
Phase 4: East Wing Offices & Courtyard $3.4 M

## Slide 43
ESTIMATE OF PROBABLE COSTS – OPTION 5 PHASED APPROACH, CONTINUED
Phase 5 & 5A: Connector, Vestibule and Entry Court
$10M
Phase 6: Post Office $1 M

## Slide 44
BANTAM OPTIONS 2A AND 5
OPTION 2A
OPTION 5

## Slide 45
COST COMPARISON OF OPTIONS 2A AND 5
Program Description:
Option 2A:
  Maintain most town hall functions in their current locations.
  Move Resident State Trooper, Police and Probate Court to Bantam Annex.
  Demolish the 1960s addition at Bantam.
Option 5:
  Maintain Town Hall functions in their current locations.
  Include 4 apartments with live/work space, compliant with the recent zoning changes.
  Probate Court is not included in this option.
Full Build Out Option 2A: $23M
(Demo 1960s Wing in Phase 1)
Phased Build Out of Option 2A: $26M (assuming 1-year intervals)
Full Build Out of Option 5: $32.8M
(with 4 Apartments)
Phased Build Out of Option 5: $37M

## Slide 46
PROGRAM OPTION E: Presented at May 22, 2024 Public Meeting #2
Expanded P&R Program
Separate buildings to provide flexibility
Arts-based Apartments
Arts Programming
Rentals require involvement in community-based arts programs.
  Classes
  Open Studios
  Gallery
  Business Development Services
ARTS-BASED LIVE / WORK SPACE
TOWN HALL CAMPUS

## Slide 47
THANK YOU
QUESTIONS & ANSWERS
“What a wonderful site! How do we avoid spoiling it?”
Marcel Breuer
Q & A and DISCUSSION
www.tlbarchitecture.com